Mercedes-Benz SL 65 AMG Black Series

Engine

| No. of cylinders/arrangement |  | 12/V, 3 valves per cylinder |
| --- | --- | --- |
| Engine displacement | cm3 | 5,980 |
| Bore x stroke | mm | 82.6 x 93.0 |
| Nominal output | kW/hp | 493/670 at 5,400 rpm |
| Nominal torque | Nm | 1000** at 2,200–4,200 rpm |
| Compression ratio |  | 9.0:1 |
| Mixture formation |  | Microprocessor-controlled petrol injection, biturbo charged |

Power transmission

| Drive train |  | Standard drive train |
| --- | --- | --- |
| Gearbox |  | AMG SPEEDSHIFT PLUS 5-speed automatic |
| Transmission ratios | Final drive 1st gear 2nd gear 3rd gear 4th gear 5th gear Reverse. | 2.65 3.60 2.19 1.41 1.00 0.83 –3.16/–1.93 |

Chassis

| Front axle | 4-link front suspension, adjustable coil-over suspension |
| --- | --- |
| Rear axle | Multi-link independent suspension, adjustable coil-over suspension |
| Brake system | Compound brake discs front and rear, internally vented and perforated, parking brake pedal, ABS, brake assist, ESP® |
| Steering | Rack and pinion power steering with parameter function, steering wheel shock absorber |
| Rims | Front: 9.5 J x 19; rear: 11.5 J x 20 |
| Tyres | Front: 265/35 ZR 19; rear: 325/30 ZR 20 |

Dimensions and weights

| Wheelbase | mm | 2,560 |
| --- | --- | --- |
| Track width, front/rear | mm | 1,684/1,658 |
| Total length | mm | 4,589 |
| Total width | mm | 1,960 |
| Total height | mm | 1,310 |
| Lock | m | 13.55 |
| Boot capacity* | l | 210 |
| Weight, ready to drive, in accordance with EC | kg | 1,870 |
| Payload (based on the following in accordance with DIN) | kg | 305 |
| Admissible total weight | kg | 2,100 |
| Tank capacity/reserve | l | 80/14.0 |

Performance and fuel consumption

| Acceleration 0–100 km/h | s | 3.8 |
| --- | --- | --- |
| Top speed | km/h | 320** |
| Total NEDC fuel consumption | l/100 km | 14.4 |

* In accordance with the VDA measuring method; ** Electronically limited

Mercedes-Benz ML 63 AMG

Engine

| No. of cylinders/arrangement |  | 8/V, 4 valves per cylinder |
| --- | --- | --- |
| Engine displacement | cm3 | 6,208 |
| Bore x stroke | mm | 102.2 x 94.6 |
| Nominal output | kW/hp | 375/510 at 6,800 rpm |
| Nominal torque | Nm | 630 at 5,200 rpm |
| Compression ratio |  | 11.3:1 |
| Mixture formation |  | Microprocessor-controlled petrol injection, HFM |

Power transmission

| Drive train |  | Permanent 4-wheel drive, moment distribution 40:60 (front/rear) |
| --- | --- | --- |
| Gearbox |  | AMG SPEEDSHIFT 7G-TRONIC |
| Transmissions | Final drive 1st gear 2nd gear 3rd gear 4th gear 5th gear 6th gear 7th gear Reverse | 3.45 4.38 2.86 1.92 1.37 1.00 0.82 0.73 –3.42/–2.23 |

Chassis

| Front axle | Double transverse link axle, brake torque support, fully supporting air suspension system with AIRMATIC level control, adaptive damping system (ADS), anti-roll bar stabiliser |
| --- | --- |
| Rear axle | 4-link axle, start-off and brake torque support, fully supporting air suspension system with AIRMATIC level control, adaptive damping system (ADS), anti-roll bar stabiliser |
| Brake system | Hydraulic dual circuit brakes with low pressure amplifier and brake assist, graduated master brake cylinder, disc brakes internally vented and perforated all round, parking brake pedal, ABS, ESP®, 4ETS |
| Steering | Rack and pinion parameter steering, steering wheel shock absorber |
| Rims | 10 J x 20 |
| Tyres | 295/40 R 20 |

Dimensions and weights

| Wheelbase | mm | 2,915 |
| --- | --- | --- |
| Track width, front/rear | mm | 1,635/1,639 |
| Total length | mm | 4,820 |
| Total width | mm | 1,951 |
| Total height | mm | 1,863 |
| Lock | m | 11.6 |
| Boot capacity* | l | 551–2,050 |
| Weight, ready to drive in accordance with EC | kg | 2,310 |
| Payload | kg | 570 |
| Admissible total weight | kg | 2,880 |
| Tank capacity/reserve | l | 95/15 |

Road performance and fuel consumption

| Acceleration 0–100 km/h | s | 5.0 |
| --- | --- | --- |
| Top speed | km/h | 250** |
| Total NEDC fuel consumption | l/100 km | 16.5 |

* In accordance with the VDA measuring method; ** Electronically limited