# Technical Data – Audi R8 Spyder 5.2 FSI quattro (386 kW)

Program for Germany – Status: September 2009

| Model | Audi R8 Spyder 5.2 FSI quattro |
| --- | --- |
| Engine / electronics |  |  |  |  |
| Engine type | 90° V10 gasoline engine with dry sump lubrication, gasoline direct injection, four-valve technology, DOHC cylinder head, intake manifold with charge movement flaps |
| Valve gear / number of valves per cylinder | Continuous intake and exhaust camshaft adjustment / 4 |
| Displacement in cc / bore x stroke in mm / compression | 5204 / 84.5 x 92.8 / 12.5 |
| Max. power output in kW (hp) / at rpm | 386 (525) / 8,000 |
| Max. torque in Nm (lb-ft) / at rpm | 530 (390) / 6,500 |
| Engine management / mixture preparation | Fully electronic engine management, Bosch MED 9.1 master/slave principle, drive-by-wire throttle control, sequential gasoline direct injection, adaptive lambda control, adaptive knock control, comfort and quick-start system, mapped ignition with solid-state high-voltage distribution |
| Exhaust emission control | Two metal primary catalytic converters, two metal main catalytic converters; four heated oxygen sensors, secondary air system |
| Emissions class | EU 4 |
| Alternator in A / battery in A/Ah | 190 / 520 / 110 |
| Drivetrain / transmission |  |  |  |  |
| Drive type | All-wheel drive, electronic differential lock (EDL), traction control (ASR), |
| Clutch | double-disk clutch 215mm diameter |
| Transmission type | 6-speed manual | R tronic sequential manual transmission |
| Gear ratio in 1st gear / 2nd gear | 4.373 / 2.709 | 4.373 / 2.709 |
| Gear ratio in 3rd gear / 4th gear | 1.925 / 1.502 | 1.925 / 1.502 |
| Gear ratio in 5th gear / 6th gear | 1.239 / 1.035 | 1.239 / 1.035 |
| Reverse gear / final drive ratio | 3.713 / 3.077 | 3.713 / 3.077 |
| Suspension / steering / brakes |  |  |  |  |
| Front suspension | Double-wishbone suspension |
| Rear suspension | Double-wishbone suspension |
| Steering / steering ratio / turning circle in meters (D102) (feet) | Hydraulic rack–and-pinion steering / 17.3 / 11.8 (38.71) |
| Brake system | Electronic stabilization program ESP with integrated ABS |
| Wheels / tires | At front: 8.5Jx19 / 235/35ZR19; at rear: 11Jx19 / 295/30ZR19 |
| Performance / consumption / acoustics |  |  |  |  |
| Top speed in km/h (mph) | 313 (194.49) | 313 (194.49) |
| Acceleration, 0-100 / 0-200 km/h (0-62.14 /0-124.27 mph) in s | 4.1 / 12.7 | 4.1 / 12.4 |
| Fuel | Super Plus RON 98 |
| Fuel consumption: city / highway / combined, l/100 km (US mpg) | 22.7/ 10.4 / 14.9 (10.36 / 22.62 / 15.79) | 20.9 / 9.9 / 13.9 (11.25 / 23.76 / 16.92) |
| CO2 mass emission, g/km (g/mile) | 543 / 249 / 356 (873.87 / 400.73 / 572.93) | 500 / 237 / 332 (804.67 / 381.41 / 534.30) |
| Idling / drive-past exterior noise level in dB (A) | 98 / 75 | 98 / 74 |
| Servicing / guarantee (Germany) |  |  |  |  |
| Oil change / inspection | According to service interval indicator up to 30,000 (18,641) (max. 2 years) 1) |
| Vehicle / paint / rust perforation guarantee | 2 years with unlimited mileage / 3 years / 12 years |
| Insurance classification in Germany: third party / fully comprehensive / part-comprehensive | 17 / 31 / 29 |
| Weights / loads |  |  |  |  |
| Unladen weight in kg (excluding driver) / gross weight limit in kg (pounds) | 1720 / 2020 (3,791.95 / 4,453.34) | 1725 / 2025 (3,802.97 / 4,464.36) |
| Axle load limit at front / rear in kg (pounds) | 970 / 1160 (2,138.48 / 2,557.36) | 970 / 1160 (2,138.48 / 2,557.36) |
| Trailer load limit, unbraked in kg (pounds) | - |
| Trailer load limit on 8% / 12% gradient, braked in kg (pounds) | - / - |
| Roof load limit in kg / permissible nose weight in kg (pounds) | - / - |
| Capacities |  |  |  |  |
| Cooling system capacity (incl. heating) in liters (US gallons) | 24 (6.34) |
| Engine oil capacity (including filter) in liters (US quarts) | 12 (12.68) |
| Fuel tank capacity in liters (US gallons) | 80 (21.13) |
| Body / dimensions |  |  |  |  |
| Body type | Audi Space Frame ASF |
| Number of doors / seats | 2 doors / 2 seats |
| Drag coefficient Cd / frontal area A in m2 (square feet) | 0.370 / 1.99 (21.42) |
| Length / width excluding mirrors / height, empty, mm (feet) | 4434 / 1904 / 1244 (14.55 / 6.25 / 4.08) |
| Wheelbase / track at front/rear, empty, mm (feet) | 2650 / 1638 / 1595 (8.69 / 5.37 / 5.23) |
| Height of loading lip, empty, mm (feet) | - |
| Luggage capacity in liters (cubic feet), according to VDA block method (V210), at front | 100 (3.53) |