## Technical Data – Audi RS 5 Coupé

Program for Germany - Status: February 2010

| Model | Audi RS 5 Coupé |
| --- | --- |
| Engine / electronics |  |
| Engine type | V8 spark-ignition engine, four-valve technology, DOHC |
| Valve gear / number of valves per cylinder | Continuous intake and exhaust camshaft adjustment, hydraulic valve play compensation with roller cam followers, 4 valves |
| Displacement in cc / bore x stroke in mm / compression | 4163 / 84.5 x 92.8 / 12.3 |
| Max. power output in kW (hp) / at rpm | 331 (450) / 8250 |
| Max. torque in Nm (lb-ft) / at rpm | 430 (317.15) / 4000 – 6000 |
| Engine management / mixture preparation | Fully electronic engine management with drive-by-wire throttle control, Bosch MED 17.1, gasoline direct injection, demand-controlled high-pressure and low-pressure fuel regulation, continuous lambda control, mapped ignition with solid-state high-voltage distribution, cylinder-selective adaptive knock control |
| Exhaust emission control | Two close-coupled ceramic catalytic converters; adaptive lambda control, each with two oxygen sensors (guiding sensor and control sensor) |
| Emissions class | EU 5 |
| Alternator in A / battery in A/Ah | 190 / 450 / 95 |
| Drivetrain / transmission |  |
| Drive type | quattro permanent all-wheel drive with self-locking crown-gear center differential and torque vectoring, electronic stabilization program (ESP) |
| Clutch | Two electrohydraulically controlled multi-plate clutches in an oil bath |
| Transmission type | 7-speed S tronic with electrohydraulic control |
| Gear ratio in 1st gear / 2nd gear | 3.692 / 2.238 |
| Gear ratio in 3rd gear / 4th gear | 1.559 / 1.175 |
| Gear ratio in 5th gear / 6th gear | 0.915 / 0.745 |
| Gear ratio in 7th gear | 0.617 |
| Reverse gear / final drive ratio | 2.944 / 4.375 |
| Suspension / steering / brakes |  |
| Front suspension | Five-link front suspension, upper and lower wishbones, tubular anti-roll bar |
| Rear suspension | Independent-wheel, trapezoidal-link rear suspension with resiliently mounted subframe, anti-roll bar |
| Steering / steering ratio / turning circle in meters (D102) (feet) | Maintenance-free rack-and-pinion steering with speed-dependent power assistance (servotronic) / 16.3 / 11.6 (38.06) |
| Brake system | 18” high-performance brake system, dual-circuit with diagonal split, ABS/EBD and ESP with brake assist; tandem brake booster; ventilated disks front and rear |
| Wheels / tires | 9J x 19 cast aluminum wheels / 265/35 R 19 |
| Performance / consumption / acoustics |  |
| Top speed in km/h (mph) | 250 (155.34) (governed) |
| Acceleration, 0-100 km/h (0-62.14 mph) in sec | 4.6 |
| Fuel | Super Plus sulfur-free, 98 RON |
| Fuel consumption: city / highway / combined, l/100 km (US mpg) | 14.9 / 8.5 / 10.8 (15.79 / 27.67 / 21.78) |
| CO2 emissions: city / highway / combined, g/km (g/mile) | 347 / 198 / 252 (558.44 / 318.65 / 405.55) |
| Idling / drive-past exterior noise level in dB (A) | 78 / 73 |
| Servicing / guarantee (Germany) |  |
| LongLife Service | Per service indicator, depending on operating conditions (max. 2 years) 1) |
| Vehicle / paint / rust perforation guarantee | 2 years with unlimited mileage / 3 years / 12 years |
| Insurance classification in Germany: third party / fully comprehensive / part-comprehensive | 19 / N28 / N30 |
| Weights / loads |  |
| Unladen weight (excluding driver)/ gross weight limit in kg (pounds) | 1725 / 2225 (3802.97 / 4905.29) |
| Axle load limit at front/rear in kg (pounds) | 1180 / 1145 (2601.45 / 2524.29) |
| Roof load limit in kg (pounds) | 75 (165.35) |
| Capacities |  |
| Cooling system capacity (incl. heating) in liters (US gallons) | 12.2 (3.22) |
| Engine oil capacity (including filter) in liters (US quarts) | 11.4 (12.05), change quantity 9.7 (10.25) |
| Fuel tank capacity in liters (US gallons) | 64 (16.91) |
| Body / dimensions 2) |  |
| Body type | Galvanized, unitary steel body, crumple zones at front and rear |
| Number of doors / seats | 2 doors with additional side protection / four seats |
| Drag coefficient Cd / frontal area A in m2 (square feet) | 0.33 / 2.18 (23.47) |
| Length (L103)/ width excluding mirrors (W103)/ height (H100-M), mm (feet) | 4649 / 1860 / 1366 (15.25 / 6.1 / 4.48) |
| Wheelbase (L101) / track at front/rear (W101-1/W102-2), mm (feet) | 2751 / 1586 / 1582 (9.03 / 5.2 / 5.19) |
| Height of loading lip in mm (H196) (feet) | 663 (2.18) |
| Luggage capacity in liters (cubic feet), according to VDA block method (V211) (V214) | 455 (1.49) |

- depends on driving style and operating conditions

- details of dimensions with unladen vehicle weight