# Technical Data – Audi R8 4.2 FSI quattro

Programme for Germany - Status: December 2006

| Model | Audi R8 4.2 FSI quattro |
| --- | --- |
| Engine / electrics |  |  |  |  |
| Engine type | Eight-cylinder V90° spark-ignition engine with dry-sump lubrication, petrol direct injection, four-valve technology, DOHC cylinder head, intake manifold with charge motion flaps |
| Valve gear / number of valves per cylinder | Continuous camshaft adjustment for the intake and exhaust valves / 4 |
| Displacement in cc / bore x stroke in mm / compression | 4163 / 84.5 x 92.8 / 12.5 |
| Max. power output in kW (bhp) / at rpm | 309 (420) / 7,800 |
| Max. torque in Nm / at rpm | 430 / 4,500 – 6,000 |
| Engine management / mixture preparation | Fully electronic engine management Bosch MED 9.1 ‘master-slave’ concept, drive-by-wire throttle control, sequential petrol direct injection, adaptive lambda control, adaptive knock control, comfort and quick-start system, mapped ignition with solid-state high-voltage distribution |
| Exhaust emission control | Two metal primary catalytic converters, two metal main catalytic converters, four heated oxygen sensors, secondary air system |
| Emissions class | EU4 |
| Alternator in A / battery in A/Ah | 190 / 520/110 |
| Drive / transmission |  |  |  |  |
| Drive type | quattro permanent four-wheel drive, electronic differential lock EDL, traction control ASR, |
| Clutch | double-plate clutch (diameter: 215 mm) |
| Gearbox type | 6-speed manual gearbox | R tronic sequential manual gearbox |
| Gear ratio in 1st gear / 2nd gear | 4.373 / 2.709 | 4.373 / 2.709 |
| Gear ratio in 3rd gear / 4th gear | 1.878 / 1.411 | 1.878 / 1.411 |
| Gear ratio in 5th gear / 6th gear / | 1.126 / 0.928 | 1.126 / 0.928 |
| Reverse gear / final drive ratio | 3.713 / 3.462 | 3.713 / 3.462 |
| Running gear / steering / brakes |  |  |  |  |
| Front suspension | Double-wishbones |
| Rear suspension | Double-wishbones |
| Steering / steering ratio / turning circle in m (D102) | Hydraulically assisted rack-and-pinion steering / 17.3 / 11.8 |
| Brake system | Electronic stabilisation program ESP with integrated ABS |
| Wheels / tyres | Front: 8.5Jx18 / 235/40 R18; rear: 10.5 Jx18 / 285/35 R18 |
| Performance / consumption / acoustics |  |  |  |  |
| Top speed in km/h | 301 | 301 |
| Acceleration 0-100 / 0-200 km/h in sec | 4.6 / 14.9 | 4.6 / 14.9 |
| Fuel grade | Super Plus 98 RON |
| Fuel consumption: urban / extra-urban / combined, l/100 km | 22.1 / 10.2 / 14.6 | 20.4 / 9.6 / 13.6 |
| CO2 mass emission, g/km | 528 / 244 / 349 | 487 / 230 / 325 |
| Standing / drive-past exterior noise level in dB (A) | 99 / 75 | 99 / 74 |
| Servicing / guarantee (Germany) |  |  |  |  |
| Oil change / inspection | According to service indicator up to 30,000 (max. 2 years) |
| Vehicle/paint/rust perforation guarantee | 2 years with unlimited mileage / 3 years / 12 years |
| Insurance classification in Germany: third party / fully comprehensive / part-comprehensive | 17 / 29 / 29 |
| Weights / loads |  |  |  |  |
| Unladen weight in kg (excl. driver) / gross weight limit in kg | 1560 / 1860 | 1565 / 1865 |
| Axle load limit at front / rear in kg | 890 / 1050 | 890 / 1055 |
| Capacities |  |  |  |  |
| Cooling system capacity (incl. heating) in l | 23 |
| Engine oil capacity (incl. filter) in l | 14.2 |
| Fuel tank capacity in l | 75 (optional: 90) |
| Body / dimensions |  |  |  |  |
| Body type | Aluminium body (ASF), boot lid and wings (plastic) |
| Number of doors / seats | 2 doors / 2 seats |
| Drag coefficient cD / frontal area A in m2 | 0.34 / 1.99 |
| Length / width excl. mirrors / height, unladen, mm | 4431 / 1904 / 1252 |
| Wheelbase / track at front/rear, mm | 2650 / 1632 / 1593 |
| Height of loading lip, unladen, mm | -- |
| Luggage capacity in l, acc. to VDA block method (V210) | 100 / 90 |